Measuring Radiation
Experiments with a Geiger-Müller Tube
N. Anna, A. Knight
University of Southern Maine Department of Physics
Measuring Radiation - Geiger-Müller Tube
March 21, 2016
1/13

---
History Behind Measuring Radiation
Geiger
In 1908, Hans Geiger theorized that one
could detect radiation by the ionized particles
Hans Geiger
in its wake...
Müller
Walther Müller devised a cheap and reliable apparatus using Geiger ’ s theory...
Walther Müller
2/13

---
Geiger-Müller Tube
The basis for all Geiger Counters
3/13

---
Relevant Information
Pros
In a sufficiently strong electric field, Townsend discharge effect ensures a count.
Cheap to manufacture and simple to operate.
Cons
Has a dead time after a each pulse, potentially missing ionizing radiation.
Cannot distinguish between radiation types, though this can be somewhat worked around by applying filters.
4/13

---
Two Experiments:
Finding Ion Chamber Region Plateau &
Determining Mass Attenuation Coefficient
5/13

---
Detector regions
6/13

---
Our Data
7/13

---
Theory in Absorption and Mass Attenuation Coefficient
Mass attenuation coefficient is a measure of how easily a material is pierced by a beam of particles, wave, energy or matter.
Follows the formula:
I(x ) = I o e −µρx
ln(I(x )) = −µρx + ln(I o )
I o : The intensity or counts with no absorption material. µ: Mass attenuation coefficient (in cm 2 ).
g
ρ: Density of material (in g
cm 3 ).
x: Thicknessofmaterial.
8/13

---
Results
Accepted Value:
µ=0.055 cg 2
Our Value:
µ=0.19±0.08
Error: 245.5%
9/13

---
Results
Accepted Value:
µ=0.059 cg 2
Our Value:
µ=0.09±0.03
Error: 52.5%
10 / 13

---
Results
Accepted Value:
µ=0.059 cg 2
Our Value:
µ=0.05±0.01
Error: 15.3%
11 / 13

---
Uncertainties
Largest error source was variation in each data collection run.
To minimize, once can take more data over shorter intervals. One research project followed this method and used a Poisson
distribution to determine the best value for each point.
There was some error during low voltages, as the potential difference was not enough to clean the ion build-up that diminished the internal electric field. This effect ceased when the voltage entered the ion chamber region.
12 / 13

---
Conclusion
Overall, this was an experiment to understand and use a new
apparatus. We explored various types of experiments that can be done using this equipment, and found both positive and negative
approaches. Our experiment produced either good data that was reasonably close to the expected value, or good insight into how to approach the experiment next time.
Some particulars:
Aβradiationsourcewouldbeabettertocalculatethemass
attenuation coefficient for aluminum. γ radiation proved to be less than effective. Our strontium source would be sufficient for this. All radiation was emitted below 2MeV, which meant the only effect was ionization. From this, we did not have to consider the
possibility of any other kind of radiation reactions in the tube. A computer program to take many data points automatically would drastically improve the uncertainty for this experiment. The limiting factor for us was simply time. Each run took from 20-60 seconds, which limited how many we could reasonably take.
13 / 13